## Slide 1
ICBT · INNOVA 2026 · IEEE COMPUTER SOCIETY
TrustFarm
Trusted AI irrigation and farm energy
Sense → Verify → Predict → Advise → Power
3D DIGITAL TWIN
TRUST-GATED AI
WASTE-TO-ENERGY
International College of Business Technology · Sri Lanka
Live demo: github.com/Ridma-kithara/TrustFarm_INNOVA
Notes: Open with the product, not the slides. This is TrustFarm: an interactive 3D farm twin, a trust gate for sensor data, a 3-hour irrigation forecast, and energy-aware advice. Everything shown is a working prototype; field results are not claimed yet.

## Slide 2
B.W.A.M. Kaushalya
Deployment & Integration
W.P.A. Rasith Maleesha
Web & Mobile Applications
B.V.D.T. Senmitha Binaragama
IoT & Communication
G.W.W.M.R. Kithara Kirinda
AI & Backend
TEAM · ICBT
Four disciplines. One integrated system.
International College of Business Technology · INNOVA 2026
TEAM OF 4
“Trust before advice.”
AI & backend · web & mobile · IoT & communication · deployment & integration
TEAM LEADER
One codebase, one demo story: sensing → trust → forecast → advice → energy.
Notes: Four members, four clear ownership areas. Kithara leads and owns AI/backend; Kaushalya owns deployment and integration; Rasith owns web and mobile; Senmitha owns IoT and communication. Avoid the old '3-member team' line.

## Slide 3
PROBLEM
Bad data becomes confident bad advice.
Low-cost field sensors fail quietly — and the model still produces an answer.
PROBLEM
01
Sensor degrades
Dirty, corroded, disconnected or stuck probes produce plausible-looking values.
02
The model trusts it
A forecast cannot tell a real soil reading from a stuck one.
03
The farmer acts
Wrong irrigation advice wastes water and erodes trust in AI.
THE GAP BETWEEN IoT AND AI
A forecast is only as trustworthy as the reading behind it.
Good data in → advice the farmer can act on.
Bad data in → a confident answer that is still wrong.
TrustFarm inserts a verification layer before the model is allowed to advise.
TrustFarm · INNOVA 2026 · ICBT
03 / 25
Notes: This is the core problem: sensor faults are silent. The system does not just need a better model; it needs a gate that decides whether the model should be allowed to speak.

## Slide 4
SDG ALIGNMENT
Trust is the enabling layer for water, food and climate action.
The project contributes to three SDGs through one operating loop.
SDG 2 · 6 · 13
2
Zero Hunger
PRIMARY FOCUS
Better irrigation decisions protect yields and reduce avoidable crop stress.
6
Clean Water
SECONDARY
Fewer wrong irrigations mean less pumped water and less waste.
13
Climate Action
SECONDARY
Farm waste is treated as an energy resource, not a disposal problem.
The measurable claim is narrower than the vision: trusted advice, less wasted water, and visible energy — validated in a pilot before savings are claimed.
TrustFarm · INNOVA 2026 · ICBT
04 / 25
Notes: Keep SDG claims proportional. The project supports SDG 2, 6 and 13 through better irrigation decisions and farm-energy visibility; it does not yet claim measured water savings.

## Slide 5
SOLUTION
One loop: sense, verify, forecast, advise, power.
Trust-gated AI plus energy-aware irrigation advice — demonstrated in a live 3D twin.
SOLUTION
SENSE
ESP32 + INA219
VERIFY
Trust Engine
PREDICT
3-hour forecast
ADVISE
Explained action
POWER
Energy gate
DATA-QUALITY GATE
The model is not always allowed to answer.
Green → advise. Amber → predict, but ask for a sensor check. Red → pause and alert.
3-HOUR FORECAST
Soil moisture, 36 steps ahead.
A GradientBoosting model forecasts soil moisture; a balanced classifier turns it into Low / Medium / High need.
ENERGY-AWARE ADVICE
Water only when power allows.
Battery state and generation can turn “irrigate now” into “delay or use manual supply”.
This is one integrated system — not three disconnected prototypes.
Status: trust engine, forecast, advice, monitoring and 3D twin are implemented. Physical energy hardware and field validation are next.
TrustFarm · INNOVA 2026 · ICBT
05 / 25
Notes: Explain the loop in one breath. The differentiator is not a single model; it is the order: verify first, then predict, then advise, then check energy. The 3D twin is the interface for the same loop.

## Slide 6
3D SYSTEM VIEW
Interactive 3D digital twin.
A real browser-based hardware model — not a rendered mock-up.
IMPLEMENTED · THREE.JS
circuit.html · actual project model · demo telemetry shown
WHAT JUDGES CAN DO
• Orbit and inspect labelled ESP32, probes, INA219, relay, battery and generator.
• Inject a fault and watch Trust turn Red; the buzzer and LED respond.
• Simulate rain or 15% battery to show wet/dry logic and PROTECT mode.
• Follow the data through animated flow particles and pin labels.
NORMAL · GREEN
FAULT · RED
RAIN
The same model is the visual language for the mobile twin on the next slide.
TrustFarm · INNOVA 2026 · ICBT
06 / 25
Notes: This is the visual proof. Open circuit.html and orbit it live if possible. The model shows the actual ESP32, two soil probes, DHT22, rain sensor, flow meter, two INA219 channels, relay, battery and biogas generator. The buttons inject a fault, rain and low battery.

## Slide 7
DIGITAL TWIN · MOBILE
The twin in your hand.
The Flutter app uses the same telemetry, trust state and 3D language.
IMPLEMENTED · FLUTTER
TAP A HOTSPOT
• ESP32 node · Green 100/100
• Soil probes · 28.4% and 29.1%
• Waste-to-energy · 78 W charging
• Battery · 74% with 14 W load
• Irrigation line · no action
OFFLINE BEHAVIOUR
The app keeps the last verified state and shows it as cached when the server is unreachable.
Preview rendered from the actual Flutter build with seeded demo data.
TrustFarm · INNOVA 2026 · ICBT
07 / 25
Notes: The mobile twin is the same product logic in a smaller form factor. Drag to orbit, tap a hotspot, and the panel shows the same numbers as the desktop build. The offline cache is real; push notifications are not.

## Slide 8
ARCHITECTURE
One system, two physical paths.
Data flows from field to advice; energy flows from waste to farm loads.
IMPLEMENTED + PROPOSED
DATA PATH
ENERGY PATH
ESP32 + sensors
soil ×2 · DHT22 · rain · flow
Mosquitto
MQTT 1883 · user + password
FastAPI + DB
ingest · SQLAlchemy · Postgres
Trust + AI
checks · forecast · advice
Apps
React web · Flutter mobile
telemetry every 60 s
REST / JSON · JWT
Organic waste
farm + food waste
Digester
sealed anaerobic
Generator
gas cleaning + generator
Controller + BMS
charge · protect
Battery → loads
12 V bank · sensors · pump
INA219 #1 generation + #2 load → FastAPI → energy mode and advice
Implemented in code: field ingest, trust gate, forecast, advice, monitoring and apps.
Proposed / supervised build: digester, gas cleaning, generator, charge controller and BMS. The code monitors; it does not control the physical energy plant.
TrustFarm · INNOVA 2026 · ICBT
08 / 25
Notes: Keep the two paths visually separate. The data path is implemented end to end. The energy path is a supervised physical build; the software monitors generation, load and battery and uses that to gate advice.

## Slide 9
TRUST ENGINE
Check the data before the model.
Three layers of checks produce a 0–100 trust score and a Green / Amber / Red decision.
IMPLEMENTED
01
Basic integrity
Missing values · impossible range · stale > 15 min · stuck for 12 readings · jump > 15 points.
02
Cross-sensor checks
Two probes disagree by > 15 (warn) or > 25 (major) · soil falls while rain is detected.
03
Learned anomaly
Isolation Forest scores the latest 5-minute window against normal behaviour.
Penalties add up. The lowest score decides the level.
score = 100 − penalties
GREEN
≥ 80
Advice allowed
AMBER
50–79
Predict, but ask for a manual check; no automatic irrigation
RED
< 50
Advice paused; alert raised; no prediction
Typical penalties: stale 60 · range 60 · missing 40 · mismatch 40/20 · stuck 35 · jump 30 · anomaly 25.
TrustFarm · INNOVA 2026 · ICBT
09 / 25
Notes: Do not describe this as a black-box AI score. It is an additive penalty system plus an Isolation Forest. Green allows advice, Amber still calls the model but the advice becomes a manual-check request, and Red returns before prediction.

## Slide 10
DECISION FLOW
From reading to recommendation.
Trust and energy both have veto power over the final advice.
IMPLEMENTED
READING
soil1/2 · temp · rain flow · battery · generation
TRUST
Green / Amber / Red score + flags
FORECAST
3 h soil moisture Low / Medium / High
ENERGY
SoC · generation PROTECT / CONSERVE
ADVICE
act · check · delay or pause
GREEN
Advice allowed
High + energy OK → “Irrigate now”. Medium → “Prepare to irrigate soon”.
AMBER
Predict, but verify
Model still runs; advice becomes “check the sensor manually”. No automatic irrigation.
RED
Stop and alert
No prediction. Advice is “sensor data not trusted”. Critical alert is raised.
Correction from the original deck: Amber still reaches the model. It is cautious guidance, not a blocked state.
TrustFarm · INNOVA 2026 · ICBT
10 / 25
Notes: This corrects a common misreading of the pipeline. Amber is not blocked; it predicts but refuses automatic action. Red is the only state that returns before prediction. The energy gate can also downgrade an irrigation action.

## Slide 11
AI FORECASTING
Three hours ahead, with safety rails.
The forecast is useful only when its inputs and limits are visible.
IMPLEMENTED · SYNTHETIC-TRAINED
1
5-min history
Recent soil, temperature, humidity, rain and flow from the last 7 hours.
2
10 features
soil · 15-min / 1-h / 6-h change · temp · humidity · rain 1 h / 6 h · hour-of-day.
3
3-hour forecast
36 steps at 5-minute resolution — corrected from the old “3 to 6 hours” claim.
4
Need class
RandomForest with balanced classes: Low / Medium / High.
5
Reason text
Rule/feature-based explanation, not SHAP. SHAP is a future extension.
SAFETY RAILS
High need < 25% soil moisture
Medium need < 35%
Wilting override < 20% forces High
STILL PLACEHOLDERS
These thresholds are global. Per-crop calibration, local soil data and SHAP explanations are explicitly future work.
Forecast target: 3 h at 5-min resolution · Baseline: persistence · Evaluation: MAE / RMSE.
TrustFarm · INNOVA 2026 · ICBT
11 / 25
Notes: This slide fixes two old claims: the horizon is 3 hours, not 3–6, and SHAP is not wired. The explanation is generated from the feature values. The thresholds are placeholders and must be tuned per crop before field use.

## Slide 12
HARDWARE
The node that produces the data.
ESP32, two soil probes, DHT22, rain, flow and dual INA219 power sensing.
FIRMWARE IMPLEMENTED
PIN / INTERFACE
SENSOR
GPIO 34
Soil probe 1 (analog)
GPIO 35
Soil probe 2 (analog)
GPIO 32
Rain sensor (wet/dry)
GPIO 27
YF-S201 flow (pulse)
GPIO 4
DHT22 temperature + humidity
I²C 0x40
INA219 generation / charger
I²C 0x41
INA219 farm load
60 s publish · 60-message ring buffer · NTP timestamps
Physical node not photographed. The image is the project’s interactive 3D wiring model; firmware is in firmware/esp32.
TrustFarm · INNOVA 2026 · ICBT
12 / 25
Notes: Use the pin table as the technical anchor. The firmware publishes every 60 seconds and buffers 60 messages if the network drops. The physical build is not evidenced in the repository, so label it as firmware-complete but hardware-pending.

## Slide 13
ENERGY
Monitor first. Automate later.
The energy layer can delay irrigation — but the prototype does not switch the pump.
MONITORING IMPLEMENTED
1
Organic waste
farm and food waste
2
Anaerobic digester
sealed, supervised
3
Gas cleaning + generator
biogas → electricity
4
Charge controller + BMS
charge and protect
5
12 V battery → loads
sensors · network · pump
3D model shown in 15% battery PROTECT state.
< 20% · PROTECT
< 40% + low gen · CONSERVE
50 W pump · energy gate
Advice only: the code never actuates the pump. Digester, generator, BMS and wiring are a supervised physical build.
TrustFarm · INNOVA 2026 · ICBT
13 / 25
Notes: This is the honest energy story. The software reads generation, load and battery, then applies 20% PROTECT and 40% CONSERVE thresholds. It does not control a BMS or switch a pump. The digester and generator are a proposed, supervised build.

## Slide 14
APPLICATIONS
One app, three views.
Live overview, 24-hour analytics and read-only alerts — on desktop and mobile.
FLUTTER · RESPONSIVE
Overview
Trust, advice, energy and the 3D hero.
Analytics
Soil, power, environment and battery.
Alerts
Critical and warning events.
IMPLEMENTED
Live dashboards · 3D twin · trust history · offline cache of last safe state.
NOT YET
Push notifications · automatic pump control · production TLS.
TrustFarm · INNOVA 2026 · ICBT
14 / 25
Notes: These are real screenshots from the Flutter build with seeded demo data. The alerts screen is read-only in this build. Push notifications and automatic pump control are not implemented; do not claim them in the demo.

## Slide 15
DATA FOUNDATION
Four datasets. One honest evidence label.
Public data supports development. It is not a substitute for a field pilot.
IEEE DATAPORT
AquaIntel
MEASURED
10.21227/tt8w-qh19
Soil moisture, water level, flow, temperature, pump status, real faults.
USED FOR
Trust engine · anomaly checks · irrigation forecasting.
AgriField-Manipur
SYNTHETIC / SIM.
10.21227/kbpa-7d35
Temperature, humidity, soil moisture, pH, rainfall, crop and district.
USED FOR
Classification features · crop/weather context.
Biogas Swine Farm
SYNTHETIC / SIM.
10.21227/jd39-y840
Biogas production, inflow, substrate and temperature time-series.
USED FOR
Energy module · scenario generation.
Semantic-Aware IoT
SYNTHETIC / SIM.
10.21227/xnk1-yn46
Soil, humidity, temperature, NPK, pH, energy and latency; 60k records.
USED FOR
IoT validation · network resilience benchmarks.
Only AquaIntel is measured hardware data. The other three are synthetic or simulated; they support development and testing, not field claims.
TrustFarm · INNOVA 2026 · ICBT
15 / 25
Notes: This slide prevents dataset inflation. AquaIntel is the one measured hardware dataset. The other three are synthetic or simulated. All four are useful for development, but none is a local field pilot.

## Slide 16
DATASET ANALYSIS · AQUAINTEL
Measured hardware data — and a very small pump signal.
AquaIntel is the strongest evidence in the current data stack.
MEASURED
WHAT THE DATASET SHOWS
2,879
baseline records
1,007
irrigation records
• Pump ON only 2% of records — a pump-state predictor would be dominated by “off”.
• Three soil types split 48.6% grey sand, 44.4% red sand, 7.0% normal; moisture and water level differ.
• Real fault labels support anomaly checks and trust-engine evaluation.
• Used for trust features, irrigation labels and forecast sanity checks.
Measured hardware dataset · IEEE DataPort 10.21227/tt8w-qh19
Charts generated from the AquaIntel dataset.
TrustFarm · INNOVA 2026 · ICBT
16 / 25
Notes: AquaIntel is the only measured hardware dataset. The key insight is the extreme class imbalance: pump ON is only 2% of records. That is why the system focuses on trust and anomaly detection rather than claiming a strong pump predictor.

## Slide 17
DATASET ANALYSIS · AGRIFIELD
Useful features, dangerous accuracy.
The irrigation labels are heavily imbalanced — so accuracy alone is misleading.
SYNTHETIC / SIMULATED
LABEL DISTRIBUTION
14,854
“No irrigation”
139
“Irrigate 800 ml”
• Rare positive class means recall and F1 matter more than headline accuracy.
• pH mean 6.45 and mean daily rain 11.3 mm — useful context, not a local calibration.
• Crop, district and weather features support classification and crop-aware rules.
• Synthetic / simulated data: use it to design the pipeline, not to claim field accuracy.
AgriField-Manipur · IEEE DataPort 10.21227/kbpa-7d35
Charts generated from the AgriField-Manipur dataset.
TrustFarm · INNOVA 2026 · ICBT
17 / 25
Notes: The AgriField dataset has 14,854 no-irrigation labels against 139 irrigate-800 ml labels. A model can look accurate by always predicting no irrigation. That is why the deck talks about recall and F1, not just accuracy.

## Slide 18
DATASET ANALYSIS · ENERGY + IOT
Two synthetic datasets, two design inputs.
Biogas gives an energy scenario; Semantic-Aware IoT gives a resilience benchmark.
SYNTHETIC / SIMULATED
BIOGAS SWINE FARM
6,281
6,269
L/day base
L/day lag model
Mean CH₄ production. Use as a scenario generator for energy-aware advice — not a yield guarantee.
SEMANTIC-AWARE IoT
60k
90.1%
55 ms
records
no migration
mean latency
Network-resilience benchmark: most records stay on the current node; latency is bounded.
Biogas charts: synthetic dataset 10.21227/jd39-y840.
TrustFarm · INNOVA 2026 · ICBT
18 / 25
Notes: Neither of these datasets is a field validation of TrustFarm. Biogas production is a scenario input for the energy module. Semantic-Aware IoT is a benchmark for edge/cloud resilience. Keep those claims separate.

## Slide 19
MODELLING
A small, auditable pipeline.
Cleaning, features, time-ordered split, training and evaluation — all in the repository.
IMPLEMENTED
CLEAN
range · missing stale · ordering
FEATURES
soil deltas · rain hour-of-day
SPLIT
time-ordered train / test
TRAIN
forecast · need anomaly
EVALUATE
MAE / RMSE precision / recall
FORECAST
GradientBoostingRegressor
10 features · 36-step horizon · persistence baseline · MAE and RMSE on a held-out time block.
NEED + ANOMALY
RandomForest + IsolationForest
Balanced class weights for Low / Medium / High. Isolation Forest is trained on normal sensor behaviour only.
No future leakage: the split is chronological. Missing values are limited-interpolated and forward-filled before feature construction.
Training code: ai_service/train.py · Serving: ai_service/app/main.py
TrustFarm · INNOVA 2026 · ICBT
19 / 25
Notes: Keep the pipeline defensible. It is not a deep-learning system. It is a gradient-boosted forecast, a balanced random forest and an isolation forest, with a chronological split and a same-as-now baseline.

## Slide 20
RESULTS
What the numbers actually show.
Forecast error improves; fault detection is still below the target.
SYNTHETIC HOLDOUT
FORECAST ERROR · LOWER IS BETTER
1.056
0.504
2.853
1.157
MAE
RMSE
baseline
model
MAE falls 52.3% and RMSE falls 59.5% against persistence. These are synthetic held-out results, not field measurements.
47.5%
sensor-fault detection
BELOW 90% TARGET
7.5%
false-alarm rate
SYNTHETIC ANOMALY TEST
99.7%
classifier accuracy
SYNTHETIC, THRESHOLD-ALIGNED
3 h
forecast horizon
36 × 5-MIN STEPS
The near-perfect classifier is expected: labels are threshold-derived. It is not evidence of field accuracy.
Do not present synthetic metrics as field performance. The next gate is a pilot with labelled sensor faults.
TrustFarm · INNOVA 2026 · ICBT
20 / 25
Notes: These numbers come from meta.json. The forecast is meaningfully better than persistence. Fault detection is 47.5%, well below the 90% target, so present it as a baseline to improve. The classifier is 99.7% on synthetic, threshold-aligned labels; that is not a field claim.

## Slide 21
SECURITY & RELIABILITY
Useful prototype. Not production-secure yet.
The honest gaps are part of the engineering plan.
PROTOTYPE
Identity & access
IMPLEMENTED
JWT sessions · farmer / officer / admin roles · per-device MQTT credentials.
Transport
GAP
MQTT on 1883 with username/password · local HTTP. TLS, restricted CORS and secret rotation are required before deployment.
Field resilience
IMPLEMENTED
ESP32 ring buffer (60 messages) · stale-reading flag · app cache of the last verified state.
Control boundary
BY DESIGN
Advice only. The relay appears in the model, but the pipeline never actuates the pump.
Known gaps to say out loud: no TLS, no push notifications, no automatic pump control, voltage-based SoC only.
TrustFarm · INNOVA 2026 · ICBT
21 / 25
Notes: This slide is deliberately blunt. The prototype has auth, roles, buffering and offline cache. It does not have TLS, push notifications, pump actuation or a proper BMS. Those are production gates, not hidden features.

## Slide 22
VALIDATION
Planned evidence, risks and exit criteria.
The pilot is the next gate. No field results are claimed yet.
TARGETS, NOT CLAIMS
VALIDATION LADDER
1
Bench calibration
raw dry/wet, two probes per zone, repeatability
2
Fault injection
stuck, spike, drift, missing, network loss
3
Model evaluation
MAE/RMSE vs persistence; High-need recall
4
Energy test
generation, charge, load, SOC estimate
5
Two-zone pilot
labelled faults and measured water/energy
RISK CONTROLS
Sensor failure
two probes, calibration, trust gate
Biogas / electrical
ventilation, gas detection, pressure relief, fuses, earthing, supervision
Data mismatch
public data for development; local data for local conclusions
Security
TLS, secret rotation, restricted CORS before deployment
SUCCESS TARGETS · not achieved yet
≥ 95%
readings received
≥ 90%
faults detected
< 3 s
dashboard response
TrustFarm · INNOVA 2026 · ICBT
22 / 25
Notes: The current synthetic fault detection is 47.5%, so the 90% target is honest but not achieved. The validation ladder moves from bench to fault injection to a two-zone pilot. Do not say 'tested in a two-zone pilot' until that actually happens.

## Slide 23
INNOVA LIVE DEMO
Six beats. One story.
Normal → fault → Red → recovery → energy constraint → 3D explanation.
DEMO SCRIPT
0:00
Normal state
Green trust, no irrigation, 3D twin live.
0:30
Inject a stuck probe
Soil probe 2 freezes; telemetry turns Red.
1:00
Advice pauses
Red state stops the recommendation and raises an alert.
1:30
Restore the sensor
Trust returns to Green; advice resumes.
2:00
Low battery
15% SOC → PROTECT; irrigation is delayed.
2:30
Orbit the 3D twin
Show pins, data flow and the energy path.
Fallback: python tools/simulator.py → s (stuck) · j (spike) · b (low battery) · n (normal). Label simulator data as simulated.
TrustFarm · INNOVA 2026 · ICBT
23 / 25
Notes: Rehearse this exact sequence. The strongest moment is not the normal dashboard; it is the transition from a plausible sensor value to a Red trust state and a paused recommendation. If hardware is unavailable, run the simulator and say so.

## Slide 24
IMPACT & NEXT GATES
A useful prototype with a clear path.
Impact is plausible; feasibility is demonstrated; field evidence is still ahead.
HONEST STAGE
IMPACT
• Fewer wrong irrigations by stopping advice on untrusted data.
• Less wasted water — target, to be measured in the pilot.
• More trust in AI because the reason and the data state are visible.
• Energy visibility links water decisions to available power.
FEASIBILITY
• 4-member team with clear ownership across AI, apps, IoT and integration.
• Open stack FastAPI, Postgres, scikit-learn, React, Flutter, Three.js.
• Local-first Docker deployment and simulator-based demos.
• Not yet a field pilot, production security or automatic pump control.
ROADMAP
NOW
3D twin · trust gate · 3h forecast · monitoring
NEXT
TLS · push alerts · per-crop calibration · two-zone pilot
LATER
Pump control with hard limits · LoRa/SMS · multi-farm cloud
The current claim is a working prototype — not a deployed farm product.
Every next step has an explicit gate: measured evidence first, then automation.
TrustFarm · INNOVA 2026 · ICBT
24 / 25
Notes: Close the argument with proportion. The impact is credible but not yet measured. Feasibility is real: the stack runs and the 3D twin works. The next gates are security, calibration and a two-zone pilot; automation comes after that.

## Slide 25
THANK YOU
Trust before advice.
Questions & live demo
Interactive 3D circuit: ridma-kithara.github.io/TrustFarm_INNOVA/circuit.html
Source: github.com/Ridma-kithara/TrustFarm_INNOVA
Team TrustFarm · ICBT · INNOVA 2026
Demo data unless hardware is connected.
Notes: End on the product principle: trust before advice. Invite the judges to orbit the circuit model or open the mobile twin, then take questions. Be explicit that the demo data is seeded unless the hardware is connected.